## Slide 1
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
SUNPOLE C
 |  | IK |  | SCx
C1 |  | 08 | 60 kg | 1.04 m²
C2 |  | 08 | 65 kg | 1.09 m²
0699_5009_E
4 x M18 anchors
Specific pole as per EN40 ø60-62 without gate
Insert height 180 mm
1

## Slide 2
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
Commissioning date
Month number
Year
Label on packing box and cassette
Commissioning must be carried out before the end of the month of the date indicated on the packaging.
Once the installation is complete, follow one of these links to declare the commissioning date.
https://forms.office.com/e/xLx8x2EAD6
If the date is exceeded, contact your ECLATEC sales agent.
For configurations with WIZARD antennas on the luminaire
which correspond to night-time profiles with fixed time dimming and/or detection, communicating detection and WIZARD remote management:
Programming must be carried out after installation and the luminaire must be powered up:
This should be done at night, or during the day after disconnecting the solar panel.
If it is not programmed, the luminaire operates at 75% of its power:
Risk of rapid battery discharge, particularly in winter (night-time profile to be programmed, often less energy-consuming).

## Slide 3
The south-facing photovoltaic panel generates electricity from solar energy during the day. The electricity produced is then stored in the battery.
Sunrise and sunset are detected by measuring the voltage at the photovoltaic panel terminals.
The photovoltaic panel does not tolerate any shade on its surface (trees, houses, etc.) that could significantly reduce electricity production and consequently be detrimental to battery charging.
The photovoltaic panel must not be exposed to artificial lighting at night. Light pollution could generate voltage at the photovoltaic panel terminals that would turn off the luminaire.
Solar lighting operation
Normal use
SOUTH
The lighting study and the unit energy sizing are determined based on average monthly sunshine values recorded over 15 consecutive years.
In the event of extended, more unfavourable sunlight conditions, the system will reduce the lighting output to increase autonomy and avoid the luminaire eventually going out altogether.
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com

## Slide 4
Delivery:
From 1 to 5 complete units, excluding poles, on non-stackable pallets.
1 unit is composed of:
1 Photovoltaic panel (PV)
1 battery cassette
1 or 2 luminaires
1 pre-assembled pole head and 1 screw kit
1 set of PV fixings
1 installation manual
Box with instructions, fuse(s), special tools, Exaboot
PV
Pole head + Screw kit
PV fixings
Luminaire
Removable battery cassette
Delivery, reception, storage, maintenance
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
Box with instructions, fuse(s), special tools, Exaboot

## Slide 5
Reception
The delivered products must be checked for conformity with the order and immediately checked for damage during transport on receipt.
Claim any damage from the carrier within 48 hours.
The battery cassette is sealed with 2 tamper-proof tapes:
Do not alter or work on the product: do not open, dismantle, immerse, short-circuit, heat, incinerate, drop or strike.
Storage:
The battery cassette must be stored horizontally in its original packaging at an ambient temperature of between +5°C and +25°C (45°C max), with relative humidity of between 15% and 65%
Do not store the units directly on the ground or near powdery materials.
Store the units in adequately ventilated premises.
Care:
Make sure the photovoltaic panel glass is kept clean at all times.
The unit, bowls and visible lenses must be cleaned regularly and rinsed with fresh water when necessary while avoiding pressurised spray.
In coastal areas, make sure the underside of the components is not contaminated with salt residue; wash at low pressure if necessary.
If installed on sites exposed to sand-bearing winds and/or salt spray, inspecting and cleaning the stand-alone unit every 2 months or less is recommended.
Checking the presence and tightness of the screws every year is recommended.
Delivery, reception, storage, maintenance
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
Tamper-proof tape
Tamper-proof tape

## Slide 6
1x SOLAR PANEL
1x BATTERY CASSETTE
Parts list
1x LUMINAIRE
OR
2x IDENTICAL LUMINAIRES
1x POLE HEAD / SINGLE OR DOUBLE LAMP INTERFACE UNIT
1x PANEL FIXING KIT
1x HARDWARE KIT
x28
x48
x20
x3
+
x4
x2
x2
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
1x Box containing
1 security key
per pallet
1 fuse per cassette
1 manual per pallet
1 PV panel disconnection tool
1 Exaboot per pallet
ZHAGA socket
Detector
OR
1 X OR 2 X
1 X OR 2 X
24V

## Slide 7
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
2
1
Assembly
3
4
5
6
230mm
Luminaire fixing
Make sure the luminaire cable is routed correctly

## Slide 8
x8
20N.m ±1
7
1
2
2
x8
x8
8
x4
x16
x8
x8
x2
x8
20N.m ±1
1
Assembly
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
The mechanical assembly must be scrupulously respected, as it guarantees the good resistance of the assembly to external stresses.

## Slide 9
10
x4
20N.m ±1
x8
x4
x4
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
x8
20N.m ±1
x16
x8
x8
1
x2
9
Assembly

## Slide 10
11
4xØ12
44Kg
49Kg
180
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com

## Slide 11
1
10N.m ±1
Orientation of the luminaire relative to the road
6x
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com

## Slide 12
1
S
6x
10N.m ±1
Orientation of the photovoltaic panel relative to the SOUTH
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com

## Slide 13
ECLATEC supply
1 key per pallet
1
3N.m ±1
1x
Battery cassette installation
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com

## Slide 14
8
1
2
It is essential to follow the connection operation order:
Luminaire(s)  Fuse  Photovoltaic panel
Risk of personal injury to the installer and irreversible damage to the equipment.
8
9
10
A
B
1’
1
Single LAMP
Dual LAMP
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
MAKE SURE TO CHECK THAT THE "24V" LABELS ARE PRESENT ON THE POWER SUPPLY WIRE AND CASSETTE BEFORE CONNECTING
SEE PAGE 6

## Slide 15
9
1
2
3
10
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
To disconnect the photovoltaic panel, use the tool supplied by ECLATEC

## Slide 16
Commissioning
If all the above steps have been followed, the system will be operational after 2 minutes.
As soon as the sun sets for the 1st time, the luminaire will light.
1
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
2
3
4
Unscrew the cassette test socket cover and connect the Exaboot harness
Connect the Exaboot box
Press the button on the Exaboot box for 2 seconds
Disconnect the Exaboot box
5
Screw the cassette test socket cover back on
Follow one of these links to declare the commissioning date:
https://forms.office.com/e/xLx8x2EAD6

## Slide 17
Troubleshooting
ECLATEC S.A.S. 41, rue Lafayette - CS 20069 - Maxéville - 54528 LAXOU CEDEX - France Tel. • + 33 (0)3 83 39 38 00
Site • www.eclatec.com
Problems | Causes | Solutions
The SUNPOLE-C lights during the day | The solar panel connector(s) are incorrectly inserted | Check that the solar panel connectors are correctly inserted into the cassette connectors.
 |  | Disconnect the solar panel from the cassette. Use a voltmeter to measure the solar panel voltage across the MC4 connector terminals. The no-load voltage must be between 34V and 42V. If the measured voltage is not within the range, contact Eclatec.
The SUNPOLE-C does not light after nightfall | The voltage delivered by the solar panel is higher than the nightfall detection voltage threshold | Wait for nightfall
 |  | Check that the panel is not illuminated by a light source
 |  | Check that the luminaire connector is correctly inserted into the cassette connector and that the clamping ring is screwed tight
 |  | Remove the male part of the fuse holder and refit it
 |  | Remove the male part of the fuse holder and disengage the fuse inside. Use a multimeter to check whether the fuse is blown
 | The luminaire is incorrectly connected or wired | Check that the luminaire connector is correctly inserted into the cassette connector and that the clamping ring is screwed tight.
 |  | Open the luminaire to check that the cable is correctly connected and that the polarity is correct. + red/brown and -blue/black
 |  | Open the luminaire to check that the LED module connectors are properly connected
The SUNPOLE-C switches off after a few days of operation | The battery is discharged | Check that the solar panel is correctly connected
 |  | Check that there are is no shade on the solar panel
 |  | Check that the solar panel is facing due SOUTH
 |  | Make sure snow does not accumulate on the solar panel in winter
 |  | In winter, wait a few days for the battery to recharge depending on the weather conditions